## Slide 1
Revisiting the Impacts of Transit Real-time Information on Waiting Time Reduction: An Empirical Analysis in Columbus, Ohio
Luyu Liu, Harvey J. Miller

## Slide 2: Real-time data is a game-changer for transit
Decreased waiting time
Decreases in total travel time
Increased transit use
Increased satisfaction
Increased security perception
……
Decreased waiting time is the most common positive finding in the literature for real-time information (RTI)

## Slide 3: Risk of missing a bus
App:
Bus delayed for 5 minutes
you should leave at 9:00am
App:
Bus delayed for 2 minutes
you should leave at 8:57am
Reclaimed delay: bus drivers compensating for being late
Discontinuity delay: RTI is not timely updated
Many RTI algorithms use a greedy strategy to aim for 0 wait time
Ignore reliability and can be risky.
Can miss the bus and wait an even longer time
Bus accelerated when you walking

## Slide 4: Avoid the risk of missing a bus
App:
Bus delayed for 5 minutes
you should leave at 9:00am
But I will leave 3 min earlier at 8:57am just in case
App:
Bus now delayed for 2 minutes
you should leave at 8:57am
Phew, just in time.
Insurance buffer: a short time buffer to decrease missing risk
It is a more prudent RTI strategy
Need to find the optimal insurance buffer for each user and time
Bus accelerated when you walking

## Slide 5: Other strategies
Follow the schedule (scheduled strategy)
No early bus policy: low risk of missing bus
May wait a long time if long delay
Leave randomly (arbitrary strategy)
Leave home randomly
Average waiting time will be half of the headway

## Slide 6: Data and methods
General Transit Feed Specification (GTFS) real-time: actual time of arrival and estimated time of arrival every 1 minutes
Automatic passenger counter data (APC): for better temporal accuracy of actual time of arrival
145, 200, 000 GTFS records, 2 TB volume
Simulate different users’ behavior for greedy, prudent, schedule, and arbitrary strategies in Python and MongoDB environment
Calculate the optimal insurance buffer for prudent RTI strategy

## Slide 7: Case study: Columbus, OH
Bus route No.2 in Central Ohio Transit Authority (COTA), Columbus, OH
Also test five other major routes for generalizability questions
(spoiler alert: it’s generalizable)

## Slide 8: Hourly average waiting time
Following schedule is close to the optimal RTI (prudent) strategy
The greedy RTI strategy’s performance is even worse than the arbitrary strategy
RTI is only useful when used properly
Headway has an impact on the waiting time and risk of missing a bus

## Slide 9: Prudent RTI strategy’s spatial pattern
Stops near the start stations (blue: higher headway; red: standard headway) have worse performance
Timepoints, where the buses must stick to the schedule, have shorter waiting time
Stops near the origin waited less than stops near the destination of the route
Higher headway service has longer wait time

## Slide 10: Compare Prudent and schedule
Upstream stops near the origin:
Less delay
Prudent is worse than schedule
Downstream stops near the destination:
More delay
Prudent is better than schedule

## Slide 11: Walking distance
Walking distance from the origin to the bus stop makes a difference for RTI strategies
For schedule and arbitrary, walking distance will not impact the arrival time and the performance
For prudent RTI, more walking time leads to more wait time
For greedy RTI, more walking time leads to less wait time

## Slide 12
Q&A

## Slide 13
Thanks!
liu.6544@osu.edu